## Slide 1: N
b
Wireless Buzzer Activation System
Powered by: • Raspberry Pi • User Datagram Protocol (UDP)
Technical highlights:
• Customizable alarm tones
• Remote Wi-Fi control
• Simple yet robust hardware design
• Instant alerts when seconds matter
[Source: instructables.com, How to Use a Buzzer]

## Slide 2: Hardware and Design
GPIO pin sends the PWM signal
1K Resistor protects the GPIO pin
NPN Transistor allows us to control the buzzer without a direct connection to the GPIO pin
Buzzer gets power from 3.3V pin on the Raspberry Pi
The frequency of the PWM signal will give the tone of the buzzer
Made with Fritzing
[Source: learn.sparkfun.com, Raspberry GPIO]

## Slide 3
Python Client Code
Implementation
Socket setup
Instantiate host address, port number
set timeout for socket
Sock
User input acceptance loop
Uses conditional logic to process and send commands
Error handling:
Catches socket timeout error and other general errors

## Slide 4: Python Server Code Implementation
GPIO Setup and Initialization
PWM Control Function
  Function interprets command received from client
UDP Socket Server
  Continuously listens for incoming messages
Seamless Exit Handling

## Slide 5: N
b
CONCLUSION
Demonstrates a reliable and low-cost solution for remote buzzer control
Utilizes the Raspberry Pi and UDP communication for efficient operation
Combines basic components with Python to make a practical IoT system
Designed to be adaptable and easy-to-implement
A solid introduction project to embedded systems and networked device communications